## Slide 1: Nvidia / CUDA
Applicability and problems
by the example
Hans Hacker

## Slide 2: Outline
Programming Model
Hardware Implementation
Memory Issues
Toolkit / SDK
Examples
  mod2am
  mod2as
Conclusion

## Slide 3: Programming Model
Define Kernels – run by N-threads in parallel
threadIdx (3 dimensional vector)
  much like rank in MPI
  Forms a thread block
Multiple blocks form a 1D- or 2D-grid
  blockIdx

## Slide 4: Hardware Implementation
Nvidia – Tesla C1060
PCIe x16 (gen 2)
(8 GB/s)
102GB/s
GT200
4 GB
GDDR3

## Slide 5: Hardware Implementation

## Slide 6
// Kernel definition
__global__ void MatAdd(float A[N][N], float B[N][N], float C[N][N]) {
int i = blockIdx.x * blockDim.x + threadIdx.x;
int j = blockIdx.y * blockDim.y + threadIdx.y;
C[i][j] = A[i][j] + B[i][j];
}
int main() {
// Kernel invocation
dim3 dimBlock(4, 4);
dim3 dimGrid( N / dimBlock.x, N / dimBlock.y );
MatAdd<<<dimGrid, dimBlock>>>(A, B, C);
}

## Slide 7: Hardware Implementation
SIMT – single-instruction multiple-thread
32 threads of each block are grouped as WARP
  All threads of a WARP execute the same line of code simultaneously
  Divergence (e.g. branches) is expensive
Memory accesses are coalesced and issued for each half-WARP

## Slide 8: Memory Issues – Global Memory
Pictures taken from Nvidia – CUDA Programming Guide
Compute capability < 1.2
Compute capability > 1.2

## Slide 9: Memory Issues – Shared Memory
Pictures taken from Nvidia – CUDA Programming Guide
no bank conflict
no bank conflict
2-way bank conflict
8-way bank conflict
no bank conflict
no or
2-way bank conflict

## Slide 10: Toolkit / SDK
Compiler / Debugger / Profiler
SDK with ready to use Examples

## Slide 11: Examples – mod2am
SP example from SDK
DP problems
  ‘-arch=sm_13‘
  Bank conflicts in shared memory
Usage of cuBLAS – SP/DP
  Column major (use transpose feature)
  Transpose-kernel from SDK
Memory Pinning

## Slide 13: Examples – mod2as
Example from Cuda Zone* (CSR kernel)
Efficient reduction (using WARP-concept)
Texture cache
Memory pinning
* "Efficient Sparse Matrix-Vector Multiplication on CUDA" by Nathan Bell and Michael Garland
// parallel reduction in shared memory
if ( lane < 16) vals [ threadIdx.x ] += vals [ threadIdx.x + 16];
if ( lane < 8) vals [ threadIdx.x ] += vals [ threadIdx.x + 8];
if ( lane < 4) vals [ threadIdx.x ] += vals [ threadIdx.x + 4];
if ( lane < 2) vals [ threadIdx.x ] += vals [ threadIdx.x + 2];
if ( lane < 1) vals [ threadIdx.x ] += vals [ threadIdx.x + 1];
// first thread writes the result
if ( lane == 0)
y[ row ] += vals [ threadIdx.x ];

## Slide 15: Conclusion
PRO
  Easy to learn C “add-on”
  Fast and efficient
    for suitable problems or
    if SDK example available
CON
  Still too unstable for reliable usage
  Too many issues to think about
  Not general purpose

## Slide 16
Thank you …
… any Questions?

## Slide 17: Examples – mod2f
32 vs. 24bit integer operations issue
float4/double2 issue
Access to shared memory slow
  Rather (re-)calculate intermediates (registers)
Avoid branches using predefined vectors