## Slide 1
GENERAL ASPECTS OF
MESOSCOPIC TRANSPORT: III
Jonathan Bird
Electrical Engineering, University at Buffalo,
Buffalo NY, USA

## Slide 2
GENERAL ASPECTS OF MESOSCOPIC TRANSPORT III
1-D Conductance Quantization … Revisited
Non-Linear Conductance of QPCs
Bias-Spectroscopy Techniques*
Breakdown of Conductance Quantization*
And Now for Something Completely … New
* UNFORTUNATELY, NO TIME FOR THIS TODAY

## Slide 3
LINEAR Conductance of
QPCs QUANTIZED in units of 2e2/h
K. J. Thomas et al. Phys. Rev. B 58, 4846 (1998)

## Slide 4
LINEAR Conductance of
QPCs QUANTIZED in units of 2e2/h
Take excess charge per unit length PER OCCUPIED SUBBAND:
ASSUMES SMALL Vsd TO AVOID NEED TO INTEGRATE OVER DoS!
This allows us to obtain the CURRENT:
But What About LARGE Voltages?

## Slide 5
GENERAL ASPECTS OF MESOSCOPIC TRANSPORT III
1-D Conductance Quantization … Revisited
Non-Linear Conductance of QPCs
Bias-Spectroscopy Techniques*
Breakdown of Conductance Quantization*
And Now for Something Completely … New
* UNFORTUNATELY, NO TIME FOR THIS TODAY

## Slide 6
A Model for the VOLTAGE DROP Across a QPC
μs
μd
1. Vsd = 0
2. Vsd > 0
qVsd
μs
μd
bqVsd
(1 – b)qVsd
BARRIER LOWERED HERE

## Slide 7
QPC Current For SINGLE
Subband Under Bias
En(ky)
ky
ms
md
ks
kd
1. Current due to SINGLE electron is evg/L
2. Current due to ALL electrons between k & k + dk
3. Thus the TOTAL current
= 0 WHEN Vsd = 0 SINCE kd = –ks

## Slide 8
QPC Current For SINGLE
Subband Under Bias
En(ky)
ky
ms
md
ks
kd
1. With Vsd applied the integral becomes
2. Since the integrand is just eVsd the DIFFERENTIAL CONDUCTANCE
JUST WHAT WE HAD BEFORE!
bqVsd
(1 – b)
qVsd

## Slide 9
QPC Current For SINGLE
Subband Under STRONG Bias
En(ky)
ky
md
ks
kd
ms
1. Now only carriers from ONE reservoir contribute to the current
2. The current is then written as
3. So the corresponding differential conductance becomes
NO LONGER QUANTIZED!

## Slide 10
QPC Current For SINGLE
Subband Under STRONG Bias

## Slide 11
HALF-PLATEAUS For A SYMMETRIC Voltage Drop (b = ½)
A. Kristensen et al., Phys. Rev. B 62, 10950 (2000)

## Slide 12
HALF-PLATEAUS Near PINCH-OFF (b << ½)
qVsd
μs
μd
bqVsd
(1 – b)qVsd
A. Kristensen et al., Phys. Rev. B 62, 10950 (2000)

## Slide 13
GENERAL ASPECTS OF MESOSCOPIC TRANSPORT III
1-D Conductance Quantization … Revisited
Non-Linear Conductance of QPCs
Bias-Spectroscopy Techniques*
Breakdown of Conductance Quantization*
And Now for Something Completely … New
* UNFORTUNATELY, NO TIME FOR THIS TODAY

## Slide 14
Determination of 1-D
Subband SPACING
N. K. Patel et al., Phys. Rev. B 44, 13549 (1991)
L. P. Kouwenhoven et al., Phys. Rev. B 39, 8040 (1991)

## Slide 15
Determination of 1-D
Subband SPACING
T. P. Martin et al., Appl. Phys. Lett. 93, 012105 (2008)
Make Use of TRANSconductance
HIGH TRANS- CONDUCTANCE
LOW TRANS- CONDUCTANCE

## Slide 16
Determination of 1-D
Subband SPACING
Make Use of TRANSconductance
A. Kristensen et al., Phys. Rev. B 62, 10950 (2000)
D = 6 meV

## Slide 17
Determination of 1-D
Subband SPACING
Typical subband spacings in the range of a FEW meV – dependent on STRUCTURE
Subband spacing typically INCREASES as gate confinement is made stronger
Bias-Spectroscopy can also be used to investigate ZEEMAN splitting of the subbands
MORE NEXT WEEK FROM ADAM MICOLICH!

## Slide 18
GENERAL ASPECTS OF MESOSCOPIC TRANSPORT III
1-D Conductance Quantization … Revisited
Non-Linear Conductance of QPCs
Bias-Spectroscopy Techniques*
Breakdown of Conductance Quantization*
And Now for Something Completely … New
* UNFORTUNATELY, NO TIME FOR THIS TODAY

## Slide 19
So Far We Have ASSUMED NO Scattering Within the QPC
Allowed SIMPLISTIC Assumption of PERFECT Transmission
SOURCE RESERVOIR
DRAIN RESERVOIR
ELECTRONS TRAVELING TO RIGHT MUST COME FROM SOURCE
ELECTRONS TRAVELING TO LEFT MUST COME FROM DRAIN

## Slide 20
Disorder in QPCs Causes
SCATTERING Between Subbands
Current in EACH channel now determined by TRANSMISSION COEFFICIENT
PROBABILITY FOR TRANSMISSION FROM SUBBAND “n” TO SUBBAND “m”
PROBABILITY FOR TRANSMISSION VIA nth SUBBAND
Current Now SAMPLE Dependent

## Slide 21
Disorder in QPCs Causes
SCATTERING Between Subbands
Calculating TOTAL Current Yields LANDAUER FORMULA
SAMPLE DEPENDENT TRANSMISSION
PROBABILITY
TRANSMISSION PROBABILITY DEPENDS STRONGLY ON THE NATURE OF THE DISORDER INSIDE THE QPC AND IS ALSO STRONGLY ENERGY DEPENDENT
CONSEQUENTLY THE CONDUCTANCE IS NO LONGER NECESSARILY QUANTIZED

## Slide 22
A Simple Limit – FIXED Transmission Per Subband
CONTACT-
RELATED RESISTANCE
DISORDER-
RELATED RESISTANCE
CAN NEVER BE ZERO
CAN BE ZERO
RESISTANCE GC-1 IS AN UNAVOIDABLE QUANTUM CONTACT RESISTANCE
RESISTANCE GD-1 IS A SAMPLE-DEPENDENT CONTRIBUTION TO THE TOTAL RESISTANCE

## Slide 23
GENERAL ASPECTS OF MESOSCOPIC TRANSPORT III
1-D Conductance Quantization … Revisited
Non-Linear Conductance of QPCs
Bias-Spectroscopy Techniques*
Breakdown of Conductance Quantization*
And Now for Something Completely … New
* UNFORTUNATELY, NO TIME FOR THIS TODAY

## Slide 24
OPTICAL Phonon Emission
at LARGE Voltages
35 meV
GaAs PHONON SPECTRUM

## Slide 25
PHONON EMISSION FOR Si
E. Pop, Nano. Res. 3, 147 (2010)

## Slide 27
Our Study - TRANSIENT
Non-Linear Transport in QPCs

## Slide 28
Our Observations:
1. REGIMES of Transient Response
QUASI-2D LIMIT
QUASI-1D LIMIT
1D LIMIT

## Slide 29
Our Observations:
2. COMPLEX Rise/Fall Times
RISE TIME FALL TIME
2 x 2e2/h

## Slide 30
Our Observations:
3. Conductance PINNING at 2e2/h!

## Slide 31
THEORETICAL Model:
PHONON-Induced Subband Mixing

## Slide 32
THEORETICAL Model:
PHONON-Induced Subband Mixing
Mixing Results in MODIFICATION of Subband Structure

## Slide 33
Mixing Results in MODIFICATION of Subband Structure

## Slide 34
In Other Words … Conductance Quantization is RESTORED at High Bias!!!