## Slide 1: Long-term optical background measurements in the Capo Passero deep-sea site
Maria Grazia Pellegriti– INFN, LNS
for the Nemo collaboration
VLVnT13 - 5-7 August 2013 AlbaNova University Center

## Slide 2: Outline
The tower deployment on March 2013
The Nemo tower instrumentation
Rate monitoring
Oceanografic instruments measurements
Conclusions
M.G. Pellegriti INFN-LNS
VLVnT13

## Slide 3
Deployment of the NEMO-Phase2 Tower from the “Nautical Tide”
The tower touches the sea-bottom at 3500m depths
Inspecting the tower with the ROV
23/03/2013 - the tower deployment
Capo Passero
+36° 17' 48.12", 15° 58' 57.00"
100 km

## Slide 4: The NEMO Phase-2 tower: main components
4 OMs/floor
2 acoustic sensors
8 floors
8 m bars, vertical dist. = 40 m, Htot = 450 m
32 OM, 16 acoustic sensors for positioning and bioacoustics (see talk of S. Viola)
oceanographic instrumentation
M.G. Pellegriti INFN-LNS
VLVnT13

## Slide 5: Off-Shore DAQ
Optical
Module
(PMT+FEM)
Anchor
Floor Control Module (FCM)
E.O.Cable
Buoy
off-shore
The OM sphere contains:
10 inch PMT (Hamamatsu R70t81)
Threshold at 0.3 s.p.e.
 The voltage supply circuit
The Front End Module (FEM)
Optical system for timing Calibration
The FEM digitizes the PMT analog signals, encodes and transmits the data to the Floor Control Module (FCM).
The signal is sampled by using two 8-bit Fast ADC running at 100 MHz (for low power dissipation) staggered by 5ns.
To match the PMT dynamic range to the ADC input, the signal level is shifted and compressed by a non-linear circuit.
Timing allignment is perfomed by using a fast optical pulser, driven by a control module, which generates short duration pulses emitted by a blue LED (sub-nasecond accuracy for offsets determination)
M.G. Pellegriti INFN-LNS
VLVnT13

## Slide 6: DAQ and slow control
on-shore
DWDM
Mux
Ethernet FCM
(eFCM)s
twin boards
Laser
to TriDAS (Trigger and Data Acq)
see talk of F. Simeone
Optical
Module
(PMT+FEM)
Anchor
Floor Control Module (FCM)
E.O.Cable
Buoy
off-shore
to Slow Control (Data Manager,
Database, Storage)
Ethernet conn.
Acoustics
M.G. Pellegriti INFN-LNS
VLVnT13

## Slide 7: PMT Counting rate
Instantaneous rate from TriDAS
Average rate from slow control
consistency checks to use average rates for monitoring
Data rates are sampled once per second by the front-end electronics
Rate measured in a time window ∆t=10ms
No “dead time” effects
Dt
1s
10 ms
15 minutes
Dead time  0
for rates < 100kHz
saturation effects
above 120 kHz
M.G. Pellegriti INFN-LNS
VLVnT13

## Slide 8
Distribution of time differences between
consecutive hits
Floor 1 PMT1
Run 412 File 0, file duration ~2h43m
M.G. Pellegriti INFN-LNS
VLVnT13
counts

## Slide 9: Rates from single events
dN/dt = A e-Δt/t
1/t = -53.7±0.2 kHz
Type-II
AfterPulses
Similar behavior and values in all OMs
Run 412 File 0, file duration ~2h43m
Floor 1 PMT1
M.G. Pellegriti INFN-LNS
VLVnT13
counts
for details on After Pulses see talk of V. Giordano

## Slide 10: Average rates from slow control
  Baseline value = 52 kHz
  Burst >100 kHz = 1.6%
Run 412 File 0, file duration ~2h43m
Floor 1 PMT1
M.G. Pellegriti INFN-LNS
VLVnT13
rate occurrence

## Slide 11: Consistency test between Slow control (SC) and TriDAS rates
S.C. and Tridas rates values show similar behavior
Percentage differences are lower then 4% in most cases.
S.C. rates are systematically larger, this is probably due to the type II after-pulse effect.
TriDAS
SC
M.G. Pellegriti INFN-LNS
VLVnT13

## Slide 12: “Old” background rate measurements
Two 8” PMTs
Threshold at 0.3 s.p.e.
First 48 hours after deployment data were collected for 5’ each 30’
Baseline 29.5 ± 2.5 kHz
Rare and sporadic events with
“instant rate” > 150kHz
NEMO 2005 results at 3500m depth in Capo Passero
Instant rate [kHz]
Instant rate [kHz]
M.G. Pellegriti INFN-LNS
12
VLVnT13

## Slide 13: Long term behavior of the background rates
Baseline (kHz)
Burst fraction > 100 kHz (%)
Floor heading (a.u.)
Time (days)
3-months
M.G. Pellegriti INFN-LNS
VLVnT13

## Slide 14
Background rates floor panoramic
Baseline (kHz)
Burst fraction > 100 kHz (%)
Horizontally outwards looking PMTs
FLOOR8 – PMT1
FLOOR8 – PMT1
Time (days)
Time (days)
FLOOR7 – PMT1
FLOOR7 – PMT1
FLOOR6 – PMT1
FLOOR6 – PMT1
FLOOR5 – PMT1
FLOOR5 – PMT1
FLOOR4 – PMT1
FLOOR4 – PMT1
FLOOR3 – PMT1
FLOOR3 – PMT1
FLOOR2 – PMT1
FLOOR2– PMT1
FLOOR1 – PMT1
FLOOR1 – PMT1

## Slide 15: Oceanografic instruments – CTD probes
CTD (Floor 1)
10 m sampling
Density (kg/m3)
Temperature (°C)
Temperature
Density
Time (days)
Current-meter data analysis in progress
Conductivity (mS/cm)
Conductivity

## Slide 16: Summary
On March the 23rd a 8-storey tower was deployed at 3500m depth and 100 km off-shore Capo Passero
Long term rate monitoring
  Very low background rates (about 60kHz)
  compatible with a 40K background with few bioluminescence bursts
Next steps
  Correlation between rates and the other instrumentation outputs (compass, CTD, current-meter)
  Long term monitoring of the site properties
M.G. Pellegriti INFN-LNS
VLVnT13