## Slide 1: Light Propagation in the South Pole Ice
Dawn Williams
University of Alabama
VLVNT 2013
Stockholm, Sweden

## Slide 2: From neutrino to DOM
Photons undergo scattering and absorption in ice
Modeling the light propagation in ice is critical to reconstructing the properties of IceCube events

## Slide 3: IceCube Calibration Devices
Muons from cosmic ray-induced air showers
Dust logger (8 locations)
12 LED flashers aboard each DOM
2 nitrogen laser “standard candles”
One camera located at the bottom of a string near the center of IceCube
(see talk by Per Olof Hulth, this session)

## Slide 4: Flasher Measurements in IceCube
Flasher data collected in 2008 during IceCube construction
40 strings active
Received charge vs. time from flashing DOMs, collected by neighboring DOMs
Solid: data
Dashed: simulation

## Slide 5: Received charge vs. depth
Depth increases with DOM number from 1450 m (DOM 1) to 2450 m (DOM 60)
Received charge is plotted for flasher at the same depth as the receiver
Strong depth-dependent variations => depth-dependent scattering and absorption due to layers of dust in the ice
Triangles: receivers ~120 m away
Circles: receivers ~215 m away

## Slide 6: Simulation
Direct photon propagation with Photon Propagation Code (PPC)
Geometric scattering coefficient b : distance between successive scatters is 1/b
Effective scattering coefficient be
Absorption coefficient a : distance travelled by photon before absorption is 1/a
Divide detector into 100 10-m layers in depth, fit to a and be in all layers (200 parameters)
Simulate many values of a and be, find best fit to data using likelihood method
θis the angle between scatters

## Slide 7: Scattering Function
Simplified Liu:
Henyey-Greenstein:
Mie:
Describes scattering on acid, mineral, salt, and soot with concentrations and radii at South Pole
Use linear combination of simplified Liu and Henyey-Greenstein models to approximate Mie Scattering

## Slide 8: Hole Ice Model
Melted and re-frozen “hole ice” introduces additional scattering
Effective scattering length of 50cm in the hole (under study)
modeled as a change in the effective angular sensitivity of the DOM
Sensitivity vs. photon angle with respect to PMT axis

## Slide 9: Results: SPICE Mie SPICE = South Pole Ice model
Absorption
Scattering
Gray band: range allowed by uncertainties: ±10%
Aartsen et al., Nucl.Instrum.Meth. A711 (2013) 73-89

## Slide 10: Likelihood
Likelihood functions using charge information only (left) and both charge and time information (right)

## Slide 11: Comparison with Dust Log Data, Tilt
Comparison of simulation to 2012 flasher data over 200 m from string 63, shows strong effect from dust layer tilt
Dust log data shows that dust layers in ice are tilted
Effective scattering from dust log agrees with value from flashers

## Slide 12: Delta T from Muons
Comparison of difference in arrival times at neighboring DOMs on a string

## Slide 13: Anisotropy in Scattering
Ratio of simulated (SPICE Mie) charge to data on strings surrounding the flashing string
Maxima of ratio histograms vs. azimuth

## Slide 14: Anisotropy

## Slide 15: Ice Model with Anisotropy: SPICE Lea
Absorption
Scattering
D. Chirkin, ICRC 2013

## Slide 16: Model error improvement
SPICE Mie flasher data/simulation comparison
SPICE Lea comparison

## Slide 17: Comparison with Muon Data
Data
SPICE Mie simulation
Ratio of data to simulation
Direction of maximum charge agrees with data from flashers

## Slide 18: Summary
Ice at the South Pole has complex depth- and x-y-dependent variations
Model fit to flasher data using direct photon propagation shows good agreement with data
Many more studies are ongoing
  Using flasher data at multiple locations in the detector
  Using multi-wavelength flasher data
  Direct simulation of the hole ice