## Slide 1: Development of a multi-PMT optical module for PINGU
L. Classen, O. Kalekin, U. Katz,
J. Reubelt, M. Tselengidou
VLVNT 2013, Stockholm
05.08.2013
PINGU
Notes: Hello. I Lew Classen, PhD in Erlangen on multi-PMT modules for PINGU, Lets look at the stuff…

## Slide 2: PINGU
Precision IceCube Next Generation Update
40 additional strings
standard optical modules
opportunity for module R&D
energy limit ~ GeV
neutrino mass hierarchy
low-mass WIMPs
physics goals
Grant 2013
example configuration
Notes: After IceCube and DeepCore, idea: increase resolution and decrease energy limit -> denser infill, goal: investigation of mass hierarchy, dark matter and R&D, one of R&D efforts are multi-PMT DOMs

## Slide 3: Multi-PMT module
www.teilchenwelt.de
IceCube & DeepCore | KM3NeT
13 inch sphere | 17 inch sphere
1  10 inch PMT | 31  3 inch PMT
Notes: on left: DOM used by IceCube, DeepCore & PNGU right: multi-PMT DOM from KM3NeT, see main difference: one big PMT vs. many smaller PMTs per DOM, fly’s eye configuration

## Slide 4: Advantages
superior photo-electron counting:
from number of hit PMTs, rather than signal waveform
angle of signal acceptance up to 4
direction sensitivity
no magnetic shielding needed
increase of sensitive area
similar overall price
per photocathode area
KM3NeT 2011
Notes: Why do that? -> Approach has some attractive features, such as photon counting from number of hit PMTs, direction sensitivity, increase of sensitive area
, all these advantages come at low extra cost, price/area similar. Especially the huge sensitive area makes it an interesting candidate for use it in MICA and for PINGU as R&D

## Slide 5: PPM-DOM
first multi-PMT DOM deployed
mounted on instrumentation line
at Antares site
opportunity of in-situ calibration
KM3NeT 2013
Notes: Good news: This concept can now prove itself: pre-production model (made from ETEL PMTs) installed at Antares instrumentation line, now collecting data. Good opportunity to do in-situ calibration of inter-PMt timing from nearby potassium-40 decays. Also possible to my tracks with one DOM already

## Slide 6: Adaptation for ice
maximum diameter: ~13 inch
temperature: - 35°C
overpressure during refreezing
reuse of 3-inch PMTs & low voltage bases
Price 2002
pressure [psi]
time [d]
Benson 2012
redesign of vessel
Notes: Can’t just plug KM3NeT DOM into ice,

## Slide 7: Cylindrical vessel
stainless steel flanges & titanium screws
wall thickness up to 18 mm
rated for 700 bar (≈ 10 000 psi)
mass (f/m): 28.2 kg/22.5kg
360 mm
390 mm (= 15.4″)
male
332 mm
female
65 mm
785 mm
Notes: That’s what came out: Cylinder vessel with hemispherical ends, connected by steel flange& screws; 390mm = 15,35inch; 332mm = 13,07inch; quite heavy; thickness varies due to production process;
Now that we know real dimensions let’s see what we can build from it…

## Slide 8: mDOM interior
segmented cylindrical vessel
41 3” PMT
main electronics in center
~ four times larger photocathode area
than standard IceCube DOM
Notes: Let’s fill in the PMTs: very crowded but 5 per layer fit in -> 21 PMTs per half cylinder; one slot left free for connector -> 41 PMTs in total; now designing holding structure, main board will be placed in center
If you do so, there comes out something like this: “mDOM”, Consists of glass cylinders with hemispherical caps, held together by metal ring structures, simulations show stability at 700 bar, sensitive area corresponds to 5 10” PMTs, length adjustable by further central segments, main advantage HUGE cathode, see dimensions, some have changed since last time

## Slide 9: PMT candidates
R12199 | D792KFL | XP53B20
Hamamatsu | ET Enterprises | HZC
180x | 12x | 2x
testing in Amsterdam, Catania, Erlangen, Patros
Notes: Current PMT candidates, started with flat PMTs, now both mushroom-shaped for better timing; right: New Chinese manufacturer, bought Photonis equipment. Prototypes being tested by different KM3NeT collaborators

## Slide 10: PMT testing status
requirements (KM3NeT) | 
quantum efficiency @ 470 nm | > 20%
transit time spread (σ, FWHM) | < 2 ns, < 4.6 ns
gain | > 2 ∙ 106
supply voltage | < 1400 V
dark count rate @ 15°C | < 1.5 kHz
peak to valley ratio | > 3
length | < 120 mm
outer diameter | ≤ 82 mm
Hamamatsu
ETEL
HZC
talk by Leonora
talk by Kalekin
Notes: Tested against predefined requirements (some of them shown here); PMTs optimized and now Hama & ETEL fulfill requirements, HZC started later, still too noisy
For details on test procedures and results see talks by Leonora & Oleg Kalekin in photodetection session

## Slide 11: Readout principle
from analogue signal to time stamped data (talks by Real & Calvo)
time
voltage
threshold
+1.5 V
signal word
start time
duration
PMT id
NIKHEF 2012
FPGA & clock
base
time
voltage
Notes: let me show you the way of the signal now: start: analogue waveform from PMT, ASIC on base applies threshold, converts to step signal,
then collected by OCTOPUS board, sent to main logic board, contains FPGA & clock (shore synchronized) & TDC, converts to digital “word”, sent to shore via fiber, have to think how to integrate into ice cube cable (twisted pair driver?)

## Slide 12: Holding structure
3D printing / rapid prototyping
adequate precision
low price (prototyping)
segmentation possible
high flexibility
alternatives considered for mass production
Notes: Have a look at holding structure: After tests with foam -> 3d printing; advantages: precise, cheap & more flexible; for prototyping: bought PLA jet printer; laser sintering for “mass” production (PPM DOM); gain experience; very flexible -> good for PINGU;
For mass production also alternative approaches
measured radioactivity for plastic material -> no significant activity in one day in E range of XXX, made of PLA or abs plastic
Vitrovex = borsilicate 3,3 glass = DURAN

## Slide 13: Module integration
Notes: learn & optimize gel handling (2 component Wacker 612); vacuum chamber for gel degassing; PMT dummies for tests; started assembling first Km3NeT DOM; Valuable experience for later mDOM intergration

## Slide 14: Angular acceptance
41 PMT mDOM
flat vs. measured PMTs
area scaled in single PMT effective areas (1 PMT ≈ 50 cm² )
flat PMT
measured PMT
14
12
10
12
10
8
Notes: Access angular acceptance of mDOM, here first approach: flat PMTs (effective area - cos) in air, little bit more sophisticated: measure intensity(angle), insert into script -> see effect; Simulations will be refined ; Later will check with real mDOM prototype; also useful for detector simulations

## Slide 15: MICA
Megaton Ice Cherenkov Array
denser instrumentation
new optical module technology
energy threshold ~ 10 MeV
Cherenkov ring imaging
supernova neutrinos
proton decay
Grant 2011
physics goals
Notes: That’s what mDOMs are for: denser infill -> Cherenkov ring imaging

## Slide 16: Detector simulations
different detector configurations
number of strings 20 – 41
framework | IceTray
ice model | SPICE-Mie
decay propagation physics | GEANT4
photon propagation | CLSim
common detector properties | 
string spacing | 7 m
OMs per string | 151
OM spacing | 2 m
height | 300 m
location | 2148 – 2448 m*
* z  [-500 m; -200 m]
Notes: Recently started corresponding simulations, here some properties & first outcomes, location below dust layer

## Slide 17: Simulated footprints
OrA
20 strings
LaSqA
41 strings
HexA
28 strings
OctA
26 strings
Notes: see different detector footprints

## Slide 18: Proton decay simulation
configuration | number of strings | number of OMs | hits / decay
OrA | 20 | 3020 | 2688
OctA | 26 | 3926 | 3592
HexA | 28 | 4228 | 3724
LaSqA | 41 | 6191 | 4354
10 proton decays generated inside cylinder
radius 10 m
x0 = 10 m
y0 = -10 m
z  [-490 m; -210 m]
p
e+ + π0
γγ
Notes: started with proton decay via this channel, first numbers indicate that simulation routine works

## Slide 19: Next steps…
build prototype for testing
radioactivity of holder & glass
low temperature behaviour
design holding structure
adaptation of electronics
Notes: here our plans to proceed on the way a first prototype; actually measurements for 1&2 done but yet but results ambiguous…

## Slide 20: Thank you for your attention!
© The Pygos Group

## Slide 21: Picture graveyard
requirements (KM3NeT) | 
quantum efficiency @ 470 nm | > 20%
transit time spread (σ, FWHM) | < 2 ns, < 4.6 ns
gain | > 2 ∙ 106
supply voltage | < 1400 V
dark count rate @ 15°C | < 1.5 kHz
cathode response inhomogeneity | < 10%
peak to valley ratio | > 3
length | < 120 mm
outer diameter | ≤ 82 mm
Hamamatsu
ETEL
HZC
talk by Leonora
talk by Kalekin